## Slide 1: PN Junction

## Slide 2
Insulator
Energy Gap ≈ 10 eV
Valence Band
Conduction Band
Valence electrons do not have enough energy to hop onto the conduction band
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 3
Conductor
Valence Band
Next higher Band
Electrons in the half-filled valence band are mobile. Hence this band is called the conduction band.
Conduction Band
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 4
Conductor
Valence Band
The next higher band and the valence band overlap. Electrons in this partially filled expanded band are mobile. Hence this expanded band is called the conduction band.
Higher Band
Conduction Band
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 5
Semiconductor (0 K)
Energy Gap ≈ 1 eV
Valence Band
Conduction Band
Semiconductors behave like insulator at absolute zero
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 6
Semiconductor (room temperature)
Energy Gap ≈ 1 eV
Valence Band
Conduction Band
Thermal agitation can provide valence electrons with energy to hop onto the conduction band
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 7
Semiconductor (higher temperature)
Energy Gap ≈ 1 eV
Valence Band
Conduction Band
Resistivity falls as temperature rises
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 8
n-type
Energy Gap ≈ 1 eV
Valence Band
Conduction Band
Doped with Group V (donor) atoms Majority charge carriers are electrons in the conduction band
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 9
p-type
Energy Gap ≈ 1 eV
Valence Band
Conduction Band
Doped with Group III (acceptor) atoms Majority charge carriers are holes in the valence band
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 10
Extrinsic n-type

## Slide 11
Extrinsic p-type

## Slide 12
N-type
Mobile Electrons (-ve) Bound Group V Dopant Ions (+ve)
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 13
N-type
Mobile Electrons (-ve) Bound Group V Dopant Ions (+ve)
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 14
P-type
Mobile Holes (+ve) Bound Group III Acceptor Ions (-ve)
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 15
P-type
Mobile Holes (+ve) Bound Group III Acceptor Ions (-ve)
Electrically neutral at every point! Current can flow both ways!
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 16
PN Junction
Diffusion (of majority carriers)
Recombination near the junction
Depletion layer (localised charges)
Barrier potential (or electric field)
P
N
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 17
Reverse Bias
P
N
Depletion layer widens
No current flow
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 18
Forward Bias
P
N
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state

## Slide 19
Forward Bias
P
N
Depletion layer narrows
Continuous current flow
Notes: An atom may have many possible energy levelts
At ordinary temperatures, most of the atoms in a sample are in the ground state